## Slide 1
KATHMANDU UNIVERSITY
Department of Computer Science and Engineering • Dhulikhel, Kavre
IoT Based
Home Automation System
Built with an ESP32 microcontroller and a self-hosted web dashboard
PROJECT TEAM
Nishant Sah
041125-25
Dipra Shrestha
041136-25
Sandesh Shrestha
041141-25
Samin Tharu
041155-25
Grishma Thapa
038007-24
Code: ENGG 102 | Year I / Sem II • July 27, 2026
Wi-Fi Link
Web Dashboard
Smart Lighting
Auto Fan Control
DHT22 Sensor
Relay Switching

## Slide 2
AGENDA
What We'll Cover
Problem & Objectives
The gap in traditional home switches and what we set out to build
System Design
Architecture, data model, and how a command flows through the system
Hardware & Software
Components used and the firmware/dashboard stack
Prototype & Testing
Breadboard build, enclosure, and validation across 5 test stages
Results & Limitations
What works today, and what the system can't do yet
Future Work & Conclusion
Voice feedback module and where this goes next
2
IoT Based Home Automation System | Kathmandu University

## Slide 3
THE PROBLEM
Traditional Switches Can't Keep Up
Most homes still rely on manual, wall-mounted switches and ageing wiring. This works, but it comes with real limitations for modern, fast-paced households:
No remote control
Appliances can only be switched at the wall — not from a phone or PC
No automation
Fans and other appliances don't respond to real temperature or humidity
Expensive commercial options
Existing smart-home kits are costly and often locked to a vendor's app
Vendor lock-in
Many systems depend on third-party cloud apps the user can't customize
3
IoT Based Home Automation System | Kathmandu University

## Slide 4
PROJECT GOALS
Objectives — All Achieved
Design and develop a smart home automation system using the ESP32 microcontroller
Control multiple electrical appliances using a 4-channel relay module through a web dashboard
Use a DHT22 sensor to automatically switch a fan on or off based on temperature and humidity
Enable remote monitoring and control of all relays through a custom web-based interface hosted on the ESP32
4
IoT Based Home Automation System | Kathmandu University

## Slide 5
RELATED WORK
How This Compares
Reference
Approach
Key Difference
Reference
Approach
Key Difference
Anusha et al. (2024)
ESP32 + relay + sensor monitoring over Wi-Fi
Reliable switching, but no self-hosted dashboard shown
Kakani et al. (2024)
ESP32 relay control via the Blynk mobile app
Convenient, but depends on a third-party app/account
This Project
ESP32 + relay + DHT22 + self-hosted dashboard + planned voice feedback
Fully independent, no cloud/app dependency
5
IoT Based Home Automation System | Kathmandu University

## Slide 6
SYSTEM DESIGN
System Architecture
The ESP32 sits at the center, bridging the user's browser, the relay-controlled appliances, and the DHT22 sensor — all over the home Wi-Fi network, with no cloud involved.
6
IoT Based Home Automation System | Kathmandu University

## Slide 7
METHODOLOGY
How It Works
1. Tap
User taps a control on the web dashboard
2. Send
Command travels over home Wi-Fi as an HTTP request
3. Process
ESP32 receives it and selects the right relay channel
4. Switch
Relay switches the appliance ON or OFF
In parallel: automatic fan control
The ESP32 continuously polls the DHT22 sensor. Whenever temperature or humidity crosses the configured threshold, it automatically toggles the fan relay and updates the dashboard — independent of any manual command.
7
IoT Based Home Automation System | Kathmandu University

## Slide 8
SYSTEM DESIGN
System Flow Diagram
8
IoT Based Home Automation System | Kathmandu University

## Slide 9
BUILD PROCESS
Methodology & Implementation Steps
1
Requirements
Analysis
2
Hardware
Selection
3
Circuit
Design
4
Web Server
Firmware
5
GPIO & Relay
Firmware
6
Sensor
Integration
7
Dashboard
UI (HTML/CSS)
8
Integration &
End-to-End Test
9
Debugging &
Optimization
10
Voice Module
(Future Phase)
Firmware developed in Embedded C/C++ using the Arduino core for ESP32; each phase was verified before moving to the next, catching issues such as GPIO mapping errors and Wi-Fi reconnect bugs early.
IoT Based Home Automation System | Kathmandu University
9

## Slide 10
COMPONENTS
Key Hardware & Software Components
HARDWARE
ESP32 Dev Board
Dual-core 240 MHz, Wi-Fi + Bluetooth, main controller
4-Channel Relay Module
5V coil, 10A/250V AC per channel
DHT22 Sensor
±0.5°C temp, ±2-5% RH, single-wire digital
I2C LCD (16×2)
Displays live Wi-Fi & status locally
5V/2A Power Supply
Powers ESP32 and relay module
Breadboard & Jumper Wires
Prototyping connections
IoT Based Home Automation System | Kathmandu University
10

## Slide 11
4-Channel Relay Module
DHT22 Sensor
IoT Based Home Automation System | Kathmandu University
11

## Slide 12
✓
✓
✓
I2C LCD (16×2)
Breadboard & Jumper Wires
IoT Based Home Automation System | Kathmandu University
12

## Slide 13
SOFTWARE & TOOLS
Arduino Core for ESP32 (C/C++) Wi-Fi, web server, GPIO, sensor firmware
HTML5 + CSS3 Dashboard structure & styling, served by ESP32
WebServer Library Routes HTTP requests to relay/sensor handlers
Adafruit DHT Sensor Library Reads DHT22 & drives auto-fan logic
Arduino IDE
Build, flash & serial debug
IoT Based Home Automation System | Kathmandu University
13

## Slide 14
TECHNICAL DESIGN
Circuit Schematic & Wiring Diagram
Signal | ESP32 Pin | Drives
Relay IN1–IN4 | D16, D17, D18, D19 | Light 1/2, Fan, Socket
DHT22 Data | GPIO 4 (D4) | Temp & humidity sensor
I2C SDA / SCL | Dedicated I2C pins | 16×2 LCD status display
IoT Based Home Automation System | Kathmandu University
14

## Slide 15
SYSTEM DESIGN
Data Model
Six entities model how a request flows from the user through the ESP32 to the relays, appliances, and sensor readings.
15
IoT Based Home Automation System | Kathmandu University

## Slide 16
IMPLEMENTATION
Prototype Build
Running breadboard prototype
ESP32, 4-channel relay, DHT22 and LCD status display, all wired and powering up.
Wooden enclosure (wood + paint work)
Compartmentalized plywood frame keeping mains wiring isolated from low-voltage electronics.
16
IoT Based Home Automation System | Kathmandu University

## Slide 17
VALIDATION
Testing, Verification & Results
Sensor Testing DHT22
✓
Network Testing Wi-Fi
IoT Based Home Automation System | Kathmandu University
17

## Slide 18
SYSTEM DESIGN
Web Dashboard Interface
Live sensor readout
Real-time temperature and humidity from the DHT22
Per-appliance toggle
Manual ON/OFF control for all 4 relay channels
Auto-mode threshold
User-configurable temperature setpoint for the fan
No app, no cloud
Served directly by the ESP32 over the home Wi-Fi network
18
IoT Based Home Automation System | Kathmandu University

## Slide 19
Integration Testing
Full System
Light, fan & socket run together, with the dashboard reflecting state in real time.
IoT Based Home Automation System | Kathmandu University
19

## Slide 20
RESULTS
What the Prototype Delivers
4
Appliances
controlled independently via relay channels
±0.5°C
Sensor accuracy
DHT22 temperature reading precision
0
Cloud services
fully self-hosted on the ESP32
5
Test stages
unit, sensor, network, dashboard, integration
Testing confirmed that relay switching, sensor readings, Wi-Fi connectivity, and the dashboard all function reliably together — meeting every objective set out in Chapter 1 of the report.
20
IoT Based Home Automation System | Kathmandu University

## Slide 21
IMPACT
Real-World Applications & Target Audience
Designed for everyday people and real-life spaces.
1
Residential Smart Homes
Makes daily life easier by allowing remote control of lights, fans, and other appliances from a phone or computer.
2
Rental Apartments
Perfect for rented spaces—no permanent wiring changes needed. Just plug, set up, and control.
3
Elderly & Senior Citizens
Allows appliances to be controlled easily without reaching wall switches, promoting safety and independence.
4
People with Disabilities
Enables greater independence by providing easy remote control of home appliances from any accessible device.
5
Students & Hobbyists
An affordable and open platform to learn, explore, and build IoT and embedded systems.
6
Small Offices & Labs
Helps automate and control appliances from one place, improving convenience & saving energy.
IoT Based Home Automation System | Kathmandu University
21

## Slide 22
HONEST ASSESSMENT
Limitations
Wi-Fi dependent
Remote/manual control is unavailable if the home wifi network goes down
No external/cloud access
Cannot be controlled from outside the local Wi-Fi network (e.g. mobile data)
Fixed threshold logic
Uses a fixed temperature threshold only.
Relay power rating
Rated for 10A/250V AC per channel — not suitable for higher-power appliances
Voice module not yet integrated
INMP441/MAX98357A wiring has started but isn't in the working prototype
Breadboard-only validation
Not yet evaluated for long-term Reliability
Not ready for Permanent Installation
22
IoT Based Home Automation System | Kathmandu University

## Slide 23
ROADMAP
Future Work & Upgrades
1
Voice Feedback Module
Uses an INMP441 microphone and MAX98357A amplifier to give voice announcements (e.g., "Fan turned on").
2
Cloud & Remote Access
Control the system from anywhere using the Internet.
3
Smart Scheduling
Set automatic ON/OFF schedules for appliances
Schedule appliances to operate automatically at specific times.
4
Dedicated Mobile App
Develop an Android/iOS(Smart Phones) app for easier control and monitoring.
5
6
IoT Based Home Automation System | Kathmandu University
23
4

## Slide 24
LIVE DEMONSTRATION
Prototype Walkthrough
Toggling appliances from the dashboard, live sensor readings, and automatic fan control — demonstrated on the physical prototype
IoT Based Home Automation System | Kathmandu University
24

## Slide 25
CONCLUSION
A Self-Hosted, Affordable Path to a Smart Home
This project set out to design and build a self-hosted, affordable home automation system around the ESP32, and the working breadboard prototype demonstrates that goal has been met. Four appliances can be controlled remotely through a custom web dashboard, a DHT22 sensor automatically manages a fan based on real environmental readings, and none of it depends on a third-party cloud service or mobile app.
All 4 objectives from Chapter 1 met and validated through testing
Fully self-hosted — no cloud dependency, no vendor lock-in
Voice-feedback module already underway as the next enhancement
25
IoT Based Home Automation System | Kathmandu University

## Slide 26
Thank You
Questions & Discussion
IoT Based Home Automation System — ENGG 102 Project Defense
PROJECT TEAM
Nishant Sah • Sandesh Shrestha • Dipra Shrestha • Samin Tharu • Grishma Thapa
Kathmandu University, Department of Computer Science and Engineering |
IoT Based Home Automation System | Kathmandu University
26

## Slide 27
Questions & Discussion
IoT Based Home Automation System | Kathmandu University
27