## Slide 1
KATHMANDU UNIVERSITY
Department of Computer Science and Engineering • Dhulikhel, Kavre
IoT Based
Home Automation System
Built with an ESP32 microcontroller and a self-hosted web dashboard
PROJECT TEAM
Nishant Sah
041125-25
Dipra Shrestha
041136-25
Sandesh Shrestha
041141-25
Samin Tharu
041155-25
Grishma Thapa
038007-24
SUBMITTED TO Mr. Santosh Shaha
Code: ENGG 102 | Year I / Sem II • July 27, 2026
Wi-Fi Link
Web Dashboard
Smart Lighting
Auto Fan Control
DHT22 Sensor
Relay Switching
Working Prototype

## Slide 2
AGENDA
What We'll Cover
Problem & Objectives
The gap in traditional home switches and what we set out to build
System Design
Architecture, data model, and how a command flows through the system
Hardware & Software
Components used and the firmware/dashboard stack
Prototype & Testing
Breadboard build, enclosure, and validation across 5 test stages
Results & Limitations
What works today, and what the system can't do yet
Future Work & Conclusion
Voice feedback module and where this goes next
IoT Based Home Automation System
2

## Slide 3
01 INTRODUCTION
Introduction & Problem Statement
Why This Project
The rapid growth of IoT has transformed how we interact with everyday living spaces.
Low-cost boards like the ESP32 combine Wi-Fi + Bluetooth, making DIY home automation more accessible than ever.
Many homes still use traditional manual switches.
Manual systems cannot be controlled remotely or automatically.
Most commercial smart-home systems are expensive and vendor-locked.
THE PROBLEM
1
No Remote Control
Traditional switches cannot be operated from a phone or PC. Or remotely.
2
Vendor Lock-In
Closed hardware and application software is used by most commercial systems.
3
High Cost
The cost of commercial smart home systems is high for many families.
4
No Climate Response
Fans and household appliances do not react automatically to temperature or humidity.
IoT Based Home Automation System | Kathmandu University
2

## Slide 4
02 RELATED WORK
Literature Review
How this project's approach compares with recent ESP32-based home automation research.
System | Control Method | Sensor-Driven Automation | Cloud / 3rd-Party Dependency
Anusha et al. (2024) | Relay module, Wi-Fi | Yes — sensor monitoring | No
Kakani et al. (2024) | Blynk mobile app | No | Yes — Blynk cloud + account
This Project | Self-hosted ESP32 web dashboard | Yes — DHT22 auto fan control | No — fully local network
Gap Identified
Existing work either depends on a third-party app/cloud for control, or offers a self-hosted dashboard with only basic on/off switching. Very few projects combine a self-hosted dashboard, sensor-driven automation, and planned voice feedback in one low-cost prototype — the gap this project addresses.
IoT Based Home Automation System | Kathmandu University
3

## Slide 5
03 GOALS
Project Objectives
1
Design a Smart Core
Design a Smart Home Automation System Using ESP32.
2
Control Appliances Remotely
Control various appliances using 4-channels relay using a web interface.
3
Automate Climate Response
Control a fan according to temperature and humidity using DHT22 sensor automatically.
4
Enable Remote Monitoring
Control all relays remotely using a web interface hosted by the ESP32.
IoT Based Home Automation System | Kathmandu University
4

## Slide 6
04 ARCHITECTURE
System Architecture
IoT Based Home Automation System | Kathmandu University
5

## Slide 7
SYSTEM DESIGN
System Flow Diagram
IoT Based Home Automation System
8

## Slide 8
05 TECHNICAL DESIGN
Circuit Schematic & Wiring Diagram
Signal | ESP32 Pin | Drives
Relay IN1–IN4 | D16, D17, D18, D19 | Light 1/2, Fan, Socket
DHT22 Data | GPIO 4 (D4) | Temp & humidity sensor
I2C SDA / SCL | Dedicated I2C pins | 16×2 LCD status display
WIRING & SAFETY NOTES
AC live/neutral wiring kept fully separate from low-voltage DC signal wiring.
5V/GND shared via breadboard power rails across ESP32, relay module & DHT22.
Relay rated 10A/250V AC per channel — fits standard household loads.
Enclosure physically isolates mains wiring from control electronics.
IoT Based Home Automation System | Kathmandu University
6

## Slide 9
06 COMPONENTS
Key Hardware & Software Components
HARDWARE
ESP32 Dev Board
Dual-core 240 MHz, Wi-Fi + Bluetooth, main controller
4-Channel Relay Module
5V coil, 10A/250V AC per channel
DHT22 Sensor
±0.5°C temp, ±2-5% RH, single-wire digital
I2C LCD (16×2)
Displays live Wi-Fi & status locally
5V/2A Power Supply
Powers ESP32 and relay module
Breadboard & Jumper Wires
Prototyping connections
IoT Based Home Automation System | Kathmandu University
7

## Slide 10
4-Channel Relay Module
DHT22 Sensor

## Slide 11
✓
✓
✓
I2C LCD (16×2)
Breadboard & Jumper Wires

## Slide 12
SOFTWARE & TOOLS
Arduino Core for ESP32 (C/C++) Wi-Fi, web server, GPIO, sensor firmware
HTML5 + CSS3 Dashboard structure & styling, served by ESP32
ESPAsyncWebServer Library Routes HTTP requests to relay/sensor handlers
Adafruit DHT Sensor Library Reads DHT22 & drives auto-fan logic
Xtensa GCC Toolchain Cross-compiles firmware for ESP32
Arduino IDE / PlatformIO + esptool Build, flash & serial debug

## Slide 13
07 BUILD PROCESS
Methodology & Implementation Steps
1
Requirements
Analysis
2
Hardware
Selection
3
Circuit
Design
4
Web Server
Firmware
5
GPIO & Relay
Firmware
6
Sensor
Integration
7
Dashboard
UI (HTML/CSS)
8
Integration &
End-to-End Test
9
Debugging &
Optimization
10
Voice Module
(Future Phase)
Firmware developed in Embedded C/C++ using the Arduino core for ESP32; each phase was verified before moving to the next, catching issues such as GPIO mapping errors and Wi-Fi reconnect bugs early.
IoT Based Home Automation System | Kathmandu University
8

## Slide 14
08 CAPABILITIES
Core Features & Functionalities
1
Remote Appliance Control
Control 4 devices (light, fan, multiplug, and socket) from any browser using the same Wi-Fi network.
2
Automatic Fan Control
Monitor temperature and humidity with a DHT22 sensor and automate the fan’s operation.
3
Live Web Dashboard
View live data from the sensors, ON/OF status of the appliances, and change the temperature threshold in one web dashboard.
4
Fully Self-Hosted
Operate all the systems on the ESP32 without using any cloud services or external applications.
SMART HOME PORTAL — LIVE UI
Actual ESP32-hosted dashboard: live temperature/humidity, per-appliance status, and auto-mode threshold control.
IoT Based Home Automation System | Kathmandu University
9

## Slide 15
09 VALIDATION
Testing, Verification & Results
Sensor Testing DHT22
✓
Network Testing Wi-Fi
IoT Based Home Automation System | Kathmandu University
10

## Slide 16
Dashboard Testing Web UI
Unit Testing Relay

## Slide 17
Integration Testing
Full System
Light, fan & socket run together, with the dashboard reflecting state in real time.

## Slide 18
10 BUDGET
Cost Analysis & Bill of Materials
Component | Qty | Est. Unit Cost (USD) | Est. Subtotal (USD)
ESP32 Dev Board | 1 | $6 – 9 | ~$8
4-Channel Relay Module | 1 | $3 – 5 | ~$4
DHT22 Temp/Humidity Sensor | 1 | $4 – 8 | ~$6
I2C LCD Display (16×2) | 1 | $3 – 5 | ~$4
5V/2A Power Supply | 1 | $3 – 5 | ~$4
Breadboard, Jumper Wires, Misc. | 1 set | $4 – 6 | ~$5
Enclosure (Plywood, Paint) | 1 | $5 – 8 | ~$6
Estimated Total | — | — | ~$37
BUDGET TAKEAWAY
~$35–40
for a fully working, self-hosted 4-appliance smart-home prototype
IoT Based Home Automation System | Kathmandu University
11

## Slide 19
11 IMPACT
Real-World Applications & Target Audience
1
Residential Smart Homes
Everyday households upgrading manual switches to remote, app-free control.
2
Rental Apartments
Non-invasive setup that plugs into existing wiring without permanent modification.
3
Elderly & Accessibility
Lets appliances be operated without reaching a wall switch, aiding mobility-limited users.
4
Students & Hobbyists
An affordable, open, and fully customizable platform for learning embedded IoT development.
5
Small Offices & Labs
Automated climate response and centralized appliance control for shared spaces.
6
Energy-Conscious Users
Automatic fan control based on real conditions helps avoid unnecessary appliance runtime.
IoT Based Home Automation System | Kathmandu University
12

## Slide 20
12 HONEST ASSESSMENT
System Limitations
!
Fully dependent on the home Wi-Fi network — if it goes down, remote/manual control from a browser is unavailable.
!
No cloud integration yet, so the system cannot be controlled or monitored from outside the local network (e.g., mobile data).
!
Automatic fan control uses a single fixed hysteresis threshold, not a configurable schedule or multi-zone logic.
!
Relay module is rated for 10A/250V AC per channel — not suited to higher-power appliances without extra hardware.
!
The voice-feedback module (INMP441/MAX98357A) is a planned enhancement, not yet integrated into the working prototype.
!
Tested on a breadboard prototype only; long-term reliability in a permanent installation has not yet been evaluated.
IoT Based Home Automation System | Kathmandu University
13

## Slide 21
13 ROADMAP
Future Work & Upgrades
1
Voice Feedback Module
INMP441 MEMS microphone + MAX98357A I2S amplifier to announce status changes aloud (e.g. "Fan turned on"). Early wiring already underway.
2
Cloud & Remote Access
Extend beyond the local network so the dashboard can be reached securely over mobile data.
3
Configurable Scheduling
Replace the single fixed threshold with a configurable schedule and multi-zone automation logic.
4
Companion Mobile App
A native or PWA mobile experience layered on top of the existing self-hosted web dashboard.
5
Energy Monitoring
Add current-sensing to track and report per-appliance power consumption over time.
6
Higher-Power Load Support
Additional hardware (contactors/SSRs) to safely extend control to higher-power appliances.
IoT Based Home Automation System | Kathmandu University
14

## Slide 22
14 IMPLEMENTATION
Prototype Build
Running breadboard prototype
ESP32, 4-channel relay, DHT22 and LCD status display, all wired and powering up.
Wooden enclosure (wood + paint work)
Compartmentalized plywood frame keeping mains wiring isolated from low-voltage electronics.
IoT Based Home Automation System
14

## Slide 23
15 LIVE DEMONSTRATION
Prototype Walkthrough
Toggling appliances from the dashboard, live sensor readings, and automatic fan control — demonstrated on the physical prototype

## Slide 24
16 RESULTS
What the Prototype Delivers
4
Appliances
controlled independently via relay channels
±0.5°C
Sensor accuracy
DHT22 temperature reading precision
0
Cloud services
fully self-hosted on the ESP32
5
Test stages
unit, sensor, network, dashboard, integration
Testing confirmed that relay switching, sensor readings, Wi-Fi connectivity, and the dashboard all function reliably together — meeting every objective set out in Chapter 1 of the report.
IoT Based Home Automation System
18

## Slide 25
Thank You
Questions & Discussion
IoT Based Home Automation System — ENGG 102 Project Proposal Defense

## Slide 26
APPENDIX
Anticipated Viva Questions
Common questions the panel may ask, with concise answers to have ready